Cleaning machine SMP MC131 The MC131 is a compact unit designed for cleaning all kinds of marine fouling from yachts and smaller ships to offshore oil & gas platforms.

Description

|  | The MC131 is a compact unit designed for cleaning all kinds of marine fouling from yachts and smaller ships to offshore oil & gas platforms. The brush rotation speed is adjustable by the diver so as to achieve an optimum hourly cleaning rate. |
| --- | --- |

Specification

|  | • Machine diameter: 235 mm • Brush diameter: 300 mm • Weight in air: 12.5 kg • Weight in seawater: 5 kg • Cleaning rate: 300 m2/hour • Depth rating: 70 m • Hydraulic requirement: 20ltr/min @ 140 bar |
| --- | --- |