DIVEX 2 DIVER HP / LP CONTROL PANEL WITH COMMUNICATIONS

The Divex 2 Diver HP / LP Control Panel with integral communications is a comprehensive surface control panel providing all the facilities necessary to monitor and control diving operations.

Ideal for inshore commercial diving and police search and rescue teams, the panel is housed within a robust carry case incorporating HP and LP air control, depth monitoring and clear communications for up to two divers.

Each diver has an independent breathing air supply which is in accordance with the Association of Diving Contractors Guidance Note ADC 5 / 95 and an electronic audio / visual alarm is fitted which alerts the surface tender when the HP air supply falls below a preset level (50 Bar).