Нydraulic power unit PP018

The PP018 hydraulic power unit is proficient for running our one and two brush units. It is an efficient and reliable power unit that is easy to handle and transport.

Specification

|  | PP018 Power Unit suitable for running MC 111/MC 131/MC 212 Oil flow: 20 l.p.m. at 1800 r.p.m. 40 l.p.m. at 3600 r.p.m. Working pressure nominal: 140 bar Pressure relief valve: Set at 160 bar Pump: Gear pump Oil temperature: Max. 70°C Hydraulic oil tank capacity: Min. 8 litres/max. 11 litres Filter system (filter cartridge): 25 Micron with by-pass Engine Vanguard 2-cylinder 18 HP 4-stroke petrol Petrol Engine oil 1.1 litres Measured sound power level LWA: 101 dB Sound pressure level 1 m LPA: 90 dB Dimensions (LxWxH) 805x625x695 mm Weight: 105 kg |
| --- | --- |